## Slide 1: WES237B: Software for Embedded Systems
Pat Pannuto
Department of Computer Science and Engineering
University of California, San Diego
Summer Session 2022

## Slide 2: Today
Morning
  SIMD recap
  Parallel Programming with CUDA
  Diving deep in CUDA, CUDA memory model & performance impact
Afternoon+
  Lab session
    GPU-accelerated image manipulation with CUDA
  Assignment
    GPU-acceleration of familiar algorithms (Sobel, BMM)

## Slide 3: Logistics
Assignment 3 due tomorrow
Assignment 4 released
  Generally: First bit of assignment is lab portion, the rest is take-home
  Finish the lab first if needed
Late policy?
  1 week: 10% off
  2 weeks: Last chance, 30% off
  Email with any exceptional circumstances, we’ll work it out

## Slide 4: Recap
Caches!
  Illusion of giant, fast memory
  Hierarchical
  Structure affects performance
Compiler Optimizations
  The compiler can do the easier stuff, but more advanced optimizations are probably on you
  Doesn’t understand algorithms
    Big O

## Slide 5: Limitations of Optimizing Compilers
Operate under fundamental constraint
Must not cause any change in program behavior
Except, possibly when program making use of nonstandard language features
Behavior that may be obvious to the programmer can be obfuscated by languages and coding styles
e.g., Data ranges may be more limited than variable types suggest
Most analysis is performed only within procedures
Whole-program analysis is too expensive in most cases
Newer versions of GCC do interprocedural analysis within individual files
But, not between code in different files
Most analysis is based only on static information
Compiler has difficulty anticipating run-time inputs
When in doubt, the compiler must be conservative​
Bryant and O'Hallaron, Computer Systems: A programmer's Perspective

## Slide 6: The guts of most interesting stuff is often ~this
void Foo(float* const A, float* const B, float* const C, const int M, const int N, const int K)
{
  for (int m = 0; m < M; m++) {
    for (int n = 0; n < N; n++) {
      for (int k = 0; k < K; k++) {
        C[m * M + n] += A[m * M + k] * B[k * K + n];
      }
    }
  }
}
And these are huge
Lab2: image.tif
480x640 pixels * 4 bytes/float ~= 1.3 MB (greyscale!)
Notes: Not literally these loops, but multi-dimensional math, which boils down to loops of basic op’s marching through arrays

## Slide 7: SIMD

## Slide 8: Flynn Taxonomy
 |  | Data Stream | 
 |  | Single | Multi
Instruction Stream | Single | SISD (Single-Core Processors) | SIMD (GPUs, Intel SSE/AVX extensions, …)
 | Multi | MISD (Dataflow architectures, Systolic Arrays [debatably], …) | MIMD (VLIW, Parallel Computers)

## Slide 9: SIMD Basics
SIMD: Single instruction multiple data
A SIMD register (or a vector register) can hold many values (2 - 16 values or more) of a single type
Each value in a SIMD register is called a SIMD lane
SIMD instructions can operate on several (typically all) values on a SIMD register

## Slide 10: SIMD
SIMD Opertions: Single Precison
%ymm0
%ymm1
vaddsd %ymm0, %ymm1, %ymm1
+
+
+
+
+
+
+
+
+
+
+
+
%ymm0
%ymm1
vaddpd %ymm0, %ymm1, %ymm1
+
+
+
+
%ymm0
%ymm1
vaddpd %ymm0, %ymm1, %ymm1
SIMD Opertions: Double Precison
Some example AVX-512F (a subset of AVX-512) instructions
Syntax
zmm0 ...zmm31 are 512 bit registers; each can hold 16 single-precision (float of C; 32 bits) or 8 double-precision (double of C; 64 bits) ﬂoating point numbers

## Slide 11: SIMD
SIMD is good at parallelizing computations doing almost exactly the same series of instructions on contiguous data
⇒ generally, main targets are simple loops whose index values can be easily identified
Original loops:
for(i=0; i<N; i++){
S(i)
}
Original loops:
for(i=0; i<N; i+=L){
S(I;i+L)
}

## Slide 12: Programming SIMD
Auto vectorization
  loop vectorization
Language extensions/directives for SIMD
  SIMD directives for loops/functions (OpenMP 4.0)
  Domain Specific Languages (Halide)
Vector types
  GCC vector extensions
Intrinsics
Assembly programming
Which vector registers is this using??

## Slide 13: Auto Vectorization
Write a loop-based code and hope compiler does (figure out) the vectorization
Int len_vec=128;
void vec_add(float *vec_A, float *vec_B, float *vec_C, int len_vec) {
int i;
for (i=0; i<len_vec; i++) {
vec_C[i] = vec_A[i] + vec_B[i];
}
}
armclang --target=aarch64-arm-none-eabi -g -c -O1 vec_add.c
Automatically performs 4 adds on
Neon extension (Neon simd register is 128 bit)
gcc -o simd_auto -march=native -O3 vec_add.c
https://www.doulos.com/knowhow/arm/using_your_c_compiler_to_exploit_neon/Resources/using_your_c_compiler_to_exploit_neon.pdf

## Slide 14: OpenMP SIMD
OpenMP simd pragma
  allows an explicit vectorization of for loops
int len_vec=128;
void vec_add(float *vec_A, float *vec_B, float *vec_C, int len_vec) {
int i;
#pragma omp simd
for (i=0; i<len_vec; i++) {
vec_C[i] = vec_A[i] + vec_B[i];
}
}

## Slide 15: GCC Vector Types
Gcc allows to define a vector types
typedef float floatv attribute ((vector size(64),aligned(sizeof(float))));
floatv x, y, z;
z += x * y;
float a, b;
floatv x, y;
y = a * x + b;
You can define operations on vector types
You can mix scalars with vector types

## Slide 16: GCC Vector Types
for (long i = 0; i < n; i += L) {
V(y[i]) = a * V(x[i]);
}
typedef float floatv attribute ((vector size(64),aligned(sizeof(float))));
#define V(lv) *((floatv*)&(lv))
for (long i = 0; i < n; i++) {
y[i] = a * x[i];
}
Notes: Compiler-native types: most portable, can be least performant

## Slide 17: Intrinsics
Processor/platform-specific functions and types
For example, ARM Neon instrinsics
#include <arm_neon.h>
https://developer.arm.com/documentation/dht0002/a/Introducing-NEON/Developing-for-NEON/Intrinsics
int16x4_t vadd_s16(int16x4_t a, int16x4_t b) {
int16x4_t c;
for (int i = 0; i < 4; i++) {
c[i] = a[i] + b[i];
}
return c;
}
Notes: Platform-native types/intrinsics: less portable, more performant – can still be beat by hand-optimized assembly in certain cases

## Slide 18: Why (auto) vectorization fails?
Potential aliasing makes auto vectorization difficult/impossible
Complex control flows make vectorization impossible or less profitable
Non-contiguous data accesses make vectorization impossible or less profitable
Giving hints to the compiler sometimes (not always) addresses the problem

## Slide 19: How do I know if my code is vectorized?
Most compilers provide tools to get a report
Add a trick to assembly (gss –S)
  enclose loops with inline assembler comments
Compiler | Report options
gcc | -fopt-info-vec-{optimized,missed}
clang | -Rpass=vectorize
asm volatile ("# xxxxxx loop begins");
for (i = 0; i < n; i++) {
... /∗ loop to be vectorized ∗/
}
asm volatile ("# xxxxxx loop ends");

## Slide 20: How do I know if my code is vectorized?
clang -O3 -Rpass=loop-vectorize -S add_vec.c -o /dev/null
add_vec.c:4:5: remark:
vectorized loop (vectorization factor: 4, unrolling interleave factor: 2)
void difficult_function_to_vecorize(int *A, int *B, int Length) {
for (int i = 0; i < Length; i++)
A[B[i]]++;
}
clang -O3 -Rpass=loop-vectorize -S difficult_to_vectorize.c -o /dev/null
difficult_to_vectorize.c:3:5: remark:
loop not vectorized: cannot identify array bounds
for (int i = 0; i < Length; i++)
^

## Slide 21: List of Optimizations & Parallel Programming

## Slide 22: Optimizations & Parallel Programming
Compiler Level Optimizations
  Loop Optimizations
    Loop fission
    Loop fusion
    Loop interchange
    Loop invariant code motion
    Loop unrolling
    …
  Data Flow Optimizations
    Common subexpression elimination
    Constant folding and propagation
    Dead store elimination
    …
  Code Generation Optimization
    Register Allocation
    Instruction Scheduling
    Instruction Selection
    Reordering computations
    ,…
Locality
  Blocking
Inline assembly
Fixed point arithmetic
SIMD NEON
Multi threading
GPU/CUDA programming

## Slide 23: Parallel Programming
And introduction to CUDA

## Slide 24: Flynn Taxonomy + CUDA?
 |  | Data Stream | 
 |  | Single | Multi
Instruction Stream | Single | SISD (Single-Core Processors) | SIMD (GPUs, Intel SSE/AVX extensions, …)
 | Multi | MISD (Dataflow architectures, Systolic Arrays [debatably], …) | MIMD (VLIW, Parallel Computers)
1.1.1. CUDA Programming Model
The CUDA Toolkit targets a class of applications whose control part runs as a process on a general purpose computing device, and which use one or more NVIDIA GPUs as coprocessors for accelerating single program, multiple data (SPMD) parallel jobs.

## Slide 25: General Purpose GPUS (GPGPUs)
GPU
  Highly parallel
  Multithreaded
  Manycore processor
GeForce 8800 GPU that supports a new programming language
  CUDA (Compute Unified Device Architecture)
Run your computational expensive modules (“kernels”) on the GPU processor
Host + Device
  Host  CPU that issues kernels
  Device  Runs the kernels
They are multithreaded SIMD architectures (SIMT: Single instruction, multiple thread )

## Slide 26: CPU (Latency) vs. GPU (Throughput)
Powerful ALU
  Reduced operation latency
Large caches
  Convert long latency memory accesses to short latency cache accesses
Sophisticated control
  Branch prediction for reduced branch latency
  Data forwarding for reduced data latency
Small caches
  To boost memory throughput
Simple control
  No branch prediction
  No data forwarding
Energy efficient ALUs
  Many, long latency but heavily pipelined for high throughput
Require massive number of threads to tolerate latencies
  Threading logic
  Thread state

## Slide 27: GPU vs. CPU
GPU is well suited for data-parallel computations
  More transistors to data processing
  Lower requirement for control flow (executed many data parallel elements)
CPU is well suited for control-centric

## Slide 28: CUDA Programming Model
Since 2006, CUDA has been used to program GPUs.
CUDA (Compute Unified Device Architecture)
  Scalable
  Lower learning curve
Scalable parallel programming model extends C and C++
Since its inception 2006, many applications are designed: Matrix solvers, sorting, face detection, seismic data processing, computational chemistry, deep learning…
Map the application into a serial and a parallel part
Host + GPU kernels
  Host CPU that launches kernels
  Kernels run the parallel part (on GPUs)

## Slide 29: CUDA
CUDA C extends C
Thread groups
Shared memories
Barrier synchronization
CUDA provides
  Fine-grained data parallelism and thread parallelism
  Coarse-grained data parallelism and task parallelism

## Slide 30: CUDA Programming Model
Serial Code
Parallel Code
Serial Code
Parallel Code
Application

## Slide 31: CUDA Programming Model
Kernel: A C program or C function for one thread
  Defined using __global__ keyword
  <<<…>>> execution configuration syntax
Thread blocks: A set of concurrent threads that execute the same thread program and may cooperate to compute a result
Grid: A set of thread blocks that execute the same kernel
Programmer must specify
  the number of threads per block
  The number of blocks for a grid
  Each thread has a private local memory
  Each thread block has a shared memory
  All threads have access to global memory

## Slide 32: CUDA Programming Model
CUDA provides three key abstractions:
  A hierarchy of thread groups
  Shared memories
  Barrier synchronization

## Slide 33: Data Parallelism - Vector Addition Example
A[0]
vector A
vector B
vector C
A[1]
A[2]
A[N-1]
B[0]
B[1]
B[2]
…
…
B[N-1]
C[0]
C[1]
C[2]
C[N-1]
…
+
+
+
+

## Slide 34: Vector Addition – Traditional C Code
// Compute vector sum C = A + B
void vecAdd(float *h_A, float *h_B, float *h_C, int n)
{
int i;
for (i = 0; i<n; i++) h_C[i] = h_A[i] + h_B[i];
}
int main()
{
// Memory allocation for h_A, h_B, and h_C
// I/O to read h_A and h_B, N elements
…
vecAdd(h_A, h_B, h_C, N);
}

## Slide 35: GPU
CPU
Host Memory
GPU
Device Memory
Part 1
Part 3
#include <cuda.h>
void vecAdd(float *h_A, float *h_B, float *h_C, int n)‏ {
int size = n* sizeof(float);
float *d_A, *d_B, *d_C;
// Part 1
// Allocate device memory for A, B, and C
// Copy A and B to device memory
// Part 2
// Kernel launch code – the device performs the actual vector addition
// Part 3
// Copy C from the device memory
// Free device vectors
}
Part 2

## Slide 36: Partial Overview of CUDA Memories
Device code can:
  R/W per-thread registers
  R/W all-shared global memory
Host code can
  Transfer data to/from per grid global memory
Host
(Device) Grid
Global
Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers

## Slide 37: Partial Overview of CUDA Memories
Host
(Device) Grid
Global
Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers
cudaMalloc()
  Allocates an object in the device global memory
  Two parameters
    Address of a pointer to the allocated object
    Size of allocated object in terms of bytes
cudaFree()
  Frees object from device global memory
  One parameter
    Pointer to freed object

## Slide 38: Partial Overview of CUDA Memories
Host
(Device) Grid
Global
Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers
cudaMemcpy()
  memory data transfer
  Requires four parameters
    Pointer to destination
    Pointer to source
    Number of bytes copied
    Type/Direction of transfer
  Transfer to device is asynchronous

## Slide 39: Partial Overview of CUDA Memories
Host
(Device) Grid
Global
Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers
void vecAdd(float *h_A, float *h_B, float *h_C, int n) {
int size = n * sizeof(float); float *d_A, *d_B, *d_C;
// Host -> Device
cudaMalloc((void **) &d_A, size);
cudaMemcpy(d_A, h_A, size, cudaMemcpyHostToDevice);
cudaMalloc((void **) &d_B, size);
cudaMemcpy(d_B, h_B, size, cudaMemcpyHostToDevice);
cudaMalloc((void **) &d_C, size);
// Kernel invocation code – to be shown later
// Device -> Host
cudaMemcpy(h_C, d_C, size, cudaMemcpyDeviceToHost);
cudaFree(d_A); cudaFree(d_B); cudaFree (d_C);
}

## Slide 40: Short memory rules
Memory Management
  Host and device memory are separate entities
  Device pointers point to GPU memory
    May be passed to/from host code
    May not be dereferenced in host code
  Host pointers point to CPU memory
    May be passed to/from device code
    May not be dereferenced in device code
Simple CUDA API for handling device memory
  cudaMalloc(), cudaFree(), cudaMemcpy()
  Similar to the C equivalents malloc(), free(), memcpy()
Slide adapted from: https://www.nvidia.com/docs/IO/116711/sc11-cuda-c-basics.pdf

## Slide 41: CUDA Arrays of Parallel Threads
A CUDA kernel is executed by a grid (array) of threads
  All threads in a grid run the same kernel code (Single Program Multiple Data)‏
  Each thread has indexes that it uses to compute memory addresses and make control decisions
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
D[i] = A[i] * B[i];
…
0
1
2
254
255
…

## Slide 42: CUDA Arrays of Parallel Threads
…
0
1
2
254
255
…
…
0
1
2
254
255
…
…
0
1
2
254
255
…
Thread Block 0
Thread Block 1
Thread Block N-1
Divide thread array into multiple blocks
  Threads within a block cooperate via shared memory and barrier synchronization
  Threads in different blocks do not interact
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
D[i] = A[i] * B[i];
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
D[i] = A[i] * B[i];
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
D[i] = A[i] * B[i];

## Slide 43: CUDA Programming Model
// Kernel definition
// __global__ is a CUDA keyword, indicates function that:
// - Runs on the device
// - Is called from host code
__global__ void VecAdd(float* A, float* B, float* C) {
int i = threadIdx.x;
C[i] = A[i] + B[i];
}
int main() {
... // memory allocation, etc
// Kernel invocation with `N` threads
// <<<…>>> is “kernel launch”; call from host to device
VecAdd<<<1, N>>>(A, B, C);
... // memory return, cleanup
}
Notes: - Each of N threads that execute VecAdd performs one pair-wise addition

## Slide 44: 1000 size vector addition
What is the X?
…
0
1
2
254
255
…
…
0
1
2
254
255
…
…
0
1
2
254
255
…
Thread Block 0
Thread Block 1
Thread Block N-1
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
D[i] = A[i] * B[i];
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
D[i] = A[i] * B[i];
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
D[i] = A[i] * B[i];

## Slide 45: Example Vector Addition: Device Code
// Compute vector sum C = A + B
// Each thread performs one pair-wise addition
__global__ void vecAddKernel(float* A, float* B, float* C, int n) {
int i = threadIdx.x + blockDim.x * blockIdx.x;
if (i < n) {
C[i] = A[i] + B[i];
}
}

## Slide 46: Host Code
void vecAdd(float* h_A, float* h_B, float* h_C, int n) {
// d_A, d_B, d_C allocations and copies omitted
vecAddKernel<<<4,256>>>(d_A, d_B, d_C, n);
}

## Slide 47: Complete example
// Compute vector sum C = A + B
// Each thread performs one pair-wise addition
__global__ void vecAddKernel(float* A, float* B, float* C, int n) {
int i = threadIdx.x + blockDim.x * blockIdx.x;
if (i < n) {
C[i] = A[i] + B[i];
}
}
void vecAdd(float* h_A, float* h_B, float* h_C, int n) {
// d_A, d_B, d_C allocations and copies omitted
vecAddKernel<<<4,256>>>(d_A, d_B, d_C, n);
}

## Slide 48: More on CUDA Function Declarations
__global__ defines a kernel function
  A kernel function must return void
__host__ is optional if used alone
__host__ __device__ float someFunc() is an option
  Generates two copies of the function! (One for each execution environment)
host
host
__host__ float HostFunc()‏
host
device
__global__ void KernelFunc()‏
device
device
__device__ float DeviceFunc()‏
Only callable from the:
Executed on the:

## Slide 49: Compiling CUDA Programs
Integrated C programs with CUDA extensions
NVCC Compiler
Host C Compiler/ Linker
Host Code
Device Code (PTX)
Device Just-in-Time Compiler
Heterogeneous Computing Platform with
CPUs, GPUs, etc.

## Slide 50: Compiling CUDA Programs
Integrated C programs with CUDA extensions
NVCC Compiler
Host C Compiler/ Linker
Host Code
Device Code (PTX)
Device Just-in-Time Compiler
Heterogeneous Computing Platform with
CPUs, GPUs, etc.
Side note: This is wild if you think about it for a moment, and gets worse as you abstract further, e.g. shaders:
https://www.cs.cornell.edu/~asampson/media/papers/opengl-snapl2017-preprint.pdf

## Slide 51: CUDA Accelerated Libraries
Linear Algebra
FFT, BLAS,
SPARSE, Matrix
Numerical & Math
RAND, Statistics
Data Struct. & AI
Sort, Scan, Zero Sum
Visual Processing
Image & Video
NVIDIA
cuFFT,
cuBLAS,
cuSPARSE
NVIDIA
Math Lib
NVIDIA cuRAND
NVIDIA
NPP
NVIDIA
Video Encode
GPU AI – Board Games
GPU AI – Path Finding
https://developer.nvidia.com/gpu-accelerated-libraries

## Slide 52: Memory in CUDA/GPU

## Slide 53: Memory Hierarchy
Each thread has its own set of registers
Group of 32 threads called a warp
  All threads in a warp execute the same instruction (SIMD)
A block (aka Threadblock, CTA) is a set of warps
A grid is a set of blocks launched as part of one kernel
  All threads in a block have fast on chip shared memory
  Threads in different block communicate via shared slow global memory
Notes: Thread = single thread.
Warp = set of threads (32) where all threads work in a lockstep (SIMD) fashion
Block = Threadblock = CTA = a set of warps
Grid = set of threadsblock launched in one kernel
Kernel = you can think of a kernel as a large parallel loop, where each thread executes one iteration
All the above are software abstractions. The real hardware contains multiple cores. These cores are split across multiple SMs (streaming multiprocessors). Threadblocks execute on the SMs.
https://www.quora.com/What-is-the-definition-of-Thread-Block-Grid-Wrap-CTA-and-SM-in-CUDA

## Slide 54: Thread and Block Hierarchy
dim3 DimGrid(3, 2); // 6 thread blocks
dim3 DimBlock(3,5,1) // 15 threads / block
Kernel <<<DimGrid, DimBlock>>> (…parallist…) ;

## Slide 55: Thread and Block Hierarchy
dim3 DimGrid(3, 2); // 6 thread blocks
dim3 DimBlock(3,5,1) // 15 threads / block
Kernel <<<DimGrid, DimBlock>>> (…parallist…) ;
Blocks and Threads are 3 dimensional
dim3 blockIdx; //Block index within a grid
dim3 threadIdx; // Thread index within a block
On modern GPUs thread block may contain up to 1024 threads
Total number of threads = Number of threads per block * Number of blocks

## Slide 56: Thread and Block Hierarchy
  gridDim, blockDim reflects the dimensions of the grid and block.
  gridDim.x, grdimDim.y and gridDim.z are 1 to 65,536
  Total number of threads in block is up to 1024
  The grid can be higher dimension than its blocks and vice versa
host
device
Kernel 1
Grid 1
Block (0, 0)
Block (1, 1)
Block (1, 0)
Block (0, 1)
Grid 2
Block (1,0)
Thread
(0,0,0)
Thread
(0,1,3)
Thread
(0,1,0)
Thread
(0,1,1)
Thread
(0,1,2)
Thread
(0,0,0)
Thread
(0,0,1)
Thread
(0,0,2)
Thread
(0,0,3)
(1,0,0)
(1,0,1)
(1,0,2)
(1,0,3)

## Slide 57: Memory and Data Locality

## Slide 58: Objective
To learn to effectively use the CUDA memory types in a parallel program
  Importance of memory access efficiency
  Registers, shared memory, global memory
  Scope and lifetime

## Slide 59: How abut Performance on a GPU
All threads access global memory for their input matrix elements
  One memory accesses (4 bytes) per floating-point addition
  4B/s of memory bandwidth/FLOPS
Assume a GPU with
  Peak floating-point rate 1,600 GFLOPS with 600 GB/s DRAM bandwidth
  4*1,600 = 6,400 GB/s required to achieve peak FLOPS rating
  The 600 GB/s memory bandwidth limits the execution at 150 GFLOPS
This limits the execution rate to 9.3% (150/1600) of the peak floating-point execution rate of the device!
Need to drastically cut down memory accesses to get close to the 1,600 GFLOPS
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory

## Slide 60: Example: Matmul
M
N
P
BLOCK_WIDTH
WIDTH
WIDTH
BLOCK_WIDTH
WIDTH
WIDTH
Row
Col

## Slide 61: Example: Matmul
P0,1
M0,2
M1,1
M0,1
M0,0
M1,0
M0,3
M1,2
P0,0
M1,3
P1,0
N3,0
N3,1
N2,1
N1,1
N0,1
N0,0
N1,0
N2,0
P1,1
P0,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
Block(0,0)
Block(0,1)
Block(1,1)
Block(1,0)
BLOCK_WIDTH = 2
Thread(0,0)
Thread(1,0)
Thread(0,1)
Thread(1,1)

## Slide 62: Memory and Registers in the Von-Neumann Model

## Slide 63: Declaring CUDA variables
Variable declaration | Memory | Scope | Lifetime
int LocalVar; | register | thread | thread
__device__ __shared__ int SharedVar; | shared | block | block
__device__ int GlobalVar; | global | grid | application
__device__ __constant__ int ConstantVar; | constant | grid | application
__device__ is optional when used with __shared__, or __constant__
Automatic variables reside in a register
  Except per-thread arrays that reside in global memory
void blurKernel(unsigned char * in, unsigned char * out, int w, int h)
{
__shared__ float ds_in[TILE_WIDTH][TILE_WIDTH];
…
}

## Slide 64: Where to declare variables?
Can host access it?
Outside of any Function
In the kernel
global
constant
register
shared

## Slide 65: Shared Memory in CUDA
A special type of memory whose contents are explicitly defined and used in the kernel source code
  One in each Streaming Multiprocessor (SM)
  Accessed at much higher speed (in both latency and throughput) than global memory
  Scope of access and sharing - thread blocks
  Lifetime – thread block, contents will disappear after the corresponding thread finishes terminates execution
  Accessed by memory load/store instructions
  A form of scratchpad memory in computer architecture
https://developer.nvidia.com/blog/using-shared-memory-cuda-cc/ has pointers to examples and details
  We’re not going to delve too deep into this particular optimization
  We start with focus on the device/host memory motion (as opposed to intra-device memory motion)

## Slide 66: Memory Locality: Tiling/Blocking

## Slide 67: Matrix Mul
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
Block(0,0)
Block(0,1)
Block(1,1)
Block(1,0)
BLOCK_WIDTH = 2
Thread(0,0)
Thread(1,0)
Thread(0,1)
Thread(1,1)

## Slide 68: Matrix Mul
Each thread accesses four elements of M and four elements of N during execution.
Among the four threads highlighted, a significant overlap occurs in the M and N elements they access. For instance, both thread0,0 and thread0,1 access M0,0 and the rest of row 0 of M. Similarly, both thread0,1 and thread1,1 access N0,1 and the rest of column 1 of N.

## Slide 69: Global Memory Access
Global Memory Access Pattern of Matrix Multiplication
Thread 1
Thread 2
…
Global Memory

## Slide 70: Tiling/Blocking
Tiling/blocking to reduce global memory access
Thread 1
Thread 2
…
Global Memory
On-chip Memory
Divide the global memory content into tiles
Focus the computation of threads on one or a small number of tiles at each point in time

## Slide 71: Tiling/Blocking
Tiling/blocking to reduce global memory access
Thread 1
Thread 2
…
Global Memory
On-chip Memory
Divide the global memory content into tiles
Focus the computation of threads on one or a small number of tiles at each point in time

## Slide 72: Tiling/Blocking

## Slide 73: Barrier Synchronization For Tiling
void __syncthreads();
Synchronizes all threads within a block
All threads must reach the barrier
  In conditional code, the condition must be uniform across the block

## Slide 74: Summary of Tiling
Identify a tile of global memory contents that are accessed by multiple threads
Load the tile from global memory into on-chip memory
Use barrier synchronization to make sure that all threads are ready to start the phase
Have the multiple threads to access their data from the on-chip memory
Use barrier synchronization to make sure that all threads have completed the current phase
Move on to the next tile

## Slide 75: SM and Warps in Detail

## Slide 76: Objective
To learn how a CUDA kernel utilizes hardware execution resources
  Assigning thread blocks to execution resources
  Capacity constraints of execution resources
  Zero-overhead thread scheduling
Reference: GPU Teaching Kit from Nvidia

## Slide 77: Transparent Scalability
Each block can execute in any order relative to others.
Hardware is free to assign blocks to any processor at any time
  A kernel scales to any number of parallel processors
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Thread grid
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
time
Reference: GPU Teaching Kit from Nvidia

## Slide 78: Example Executing Thread Blocks
Threads are assigned to Streaming Multiprocessors (SM) in block granularity
  In Volta GPU, up to 32 blocks to each SM as resource allows
  Volta SM can take up to 2048 threads
    Could be 256 (threads/block) * 8 blocks
    Or 512 (threads/block) * 4 blocks, etc.
SM maintains thread/block idx (s)
SM manages/schedules thread execution
t0 t1 t2 … tm
Blocks
SP
Shared
Memory
SM
Reference: GPU Teaching Kit from Nvidia

## Slide 79: The Von-Neumann Model
Reference: GPU Teaching Kit from Nvidia

## Slide 80: The Von-Neumann Model with SIMD units
Reference: GPU Teaching Kit from Nvidia

## Slide 81: Warps as Scheduling Units
Each Block is executed as 32-thread Warps
  An implementation decision, not part of the CUDA programming model
  Warps are scheduling units in SM
  Threads in a warp execute in SIMD
  Future GPUs may have different number of threads in each warp
Reference: GPU Teaching Kit from Nvidia

## Slide 82: Warp Example
If 3 blocks are assigned to an SM and each block has 256 threads, how many Warps are there in an SM?
  Each Block is divided into 256/32 = 8 Warps
  There are 8 * 3 = 24 Warps
SM implements zero-overhead warp scheduling
  Warps whose next instruction has its operands ready for consumption are eligible for execution
  Eligible Warps are selected for execution based on a prioritized scheduling policy
  All threads in a warp execute the same instruction when selected
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 0 Warps
Block 1 Warps
…
t0 t1 t2 … t31
…
Block 2 Warps
Register File
L1
Shared Memory
Reference: GPU Teaching Kit from Nvidia

## Slide 83: Block Granularity Considerations
For Matrix Multiplication using multiple blocks, should each block have 4X4, 8X8 or 30X30 threads for Volta?
  For 4X4, we have 16 threads per Block. Each SM can take up to 2048 threads, which translates to 128 Blocks. However, each SM can only take up to 32 Blocks, so only 512 threads will go into each SM!
  For 8X8, we have 64 threads per Block. Since each SM can take up to 2048 threads, it can take up to 32 Blocks and achieve full capacity unless other resource considerations overrule.
  For 30X30, we would have 900 threads per Block. Only two blocks could fit into an SM for Volta, so only 1800/2048 of the SM thread capacity would be utilized.
Reference: GPU Teaching Kit from Nvidia

## Slide 84: Next Time
Parallel Programming Patterns
Streaming Programming Patterns
Deep Learning (Lite)